## Slide 1: Krill Capture Device
Sev Clarke, Feb 2022

## Slide 2
Capture device design
Frangible cap made
from toughened,
thick, automobile
windscreen glass
Small, explosive charge
fragments glass and
stuns nearby krill
Tapered, resealing, sliding door
secured by narrowing rails
Support cable &
comms from ship
Rosette of
capture tubes
Video cameras
and lights, 6/3
down/up
Krill bloom
Annular end plate
welded on to ss
tubes
Doubly wedge-shaped, spring-loaded,
sliding door reseals each activated
sampling tube ~2 seconds after glass cap fragments, giving time
for the sampling tube to fill
Annular ss plate secures
the base of the rosette
Tubes welded to plate
Annular grooves containing
O-rings to seal the tubes
Door thickness narrows here
to a slightly wedge shape
Frangible, ~3L glass containers
for a preserving fluid, such
as ethanol, formalin
or formaldehyde
Vacuum
Spigot for
evacuation
Ballast
Cylindrical, stainless steel capture
tube,~1.3m long by 22cm OD