## Slide 1: Helping Methanotrophs To Reduce Methane Emissions
Sev Clarke, May 2021

## Slide 2: How to use buoyant flakes to help prevent global warming by atmospheric methane
Methane-eating microorganisms (bacteria), or methanotrophs, live in most places (in water, soil, mud and rock) but flourish only when there is a steady supply of methane, the other nutrients to help them grow, and the sometimes-rare trace elements necessary for making the enzymes that permit methane digestion (metabolization).
Different methanotrophic species operate in anoxic, hypoxic and oxygen-rich environments. These are broadly classified as being either aerobic or anaerobic. Many methanotrophs operate best at the oxic-anoxic interface. Most are inhibited by illumination over 150 microeinsteins/m2/s (see Dumestre et al. 1999).
Frigid water methanotrophs require a slightly different nutrient mix, one that includes tungsten.
In soil, swamp, lake, marine and seabed environments, methanotrophs flourish best if the methane is in either dissolved form or is in the form of tiny bubbles that may rise, if at all, only slowly and where the nutrients they require are available throughout the water column and ooze.
Buoyant flakes on the water surface are in the best position steadily to release their nutrients that sink slowly, suffusing the environments below.
Methanotrophs are different from phytoplankton that use sunlight and carbon dioxide as their carbon source. Both types help form the basis of the marine food web.
The following experiments are designed to establish the optimal parameters under which methanotrophs can metabolize ebullient (bubbling) methane such that it is formed into biomass rather than contributing to global warming in the atmosphere.

## Slide 3: Elements of the Experiment
Two, tall (perhaps up to 6.5m long), preferably-transparent polymeric pipe mesocosms, sealed at the base and enclosing ooze, water, buoyant flakes and gas. Only the buoyant flakes for the experimental mesocosm contain the minerals necessary for production of methane-converting enzymes. The others just standard ones.
The solid and liquid contents of each mesocosm may be sourced from places like swamps, hypoxic seabed or where there are aquatic emissions of methane. Baltic or estuarine mud and water might be useful sources.
Sitting in or on the ooze of each mesocosm is a diffuser that can intermittently generate tiny bubbles of methane for both the experimental mesocosm and the control mesocosm. Each mesocosm is given methane at the same accurately-measured rate. A proportion of oxygen may be needed with the methane or else the presence of sulphate in the ooze or seawater by which methane oxidation may occur anaerobically by methanotrophs.
Each mesocosm is capped with a deflated bag or balloon that inflates as more gas is introduced to the mesocosm by the bubbling. Korean researchers have developed a diffuser nozzle capable of generating suitable microbubbles
Lamps above may be used to simulate sunlit (including the UV that helps flake degradation) or dark operation. Alternatively, agitation of the flakes in the dark might be used to generate mutual abrasion.
A gas analyzer is used progressively to determine the varying methane and CO2 concentrations in each bag.
The volume of each bag is also progressively measured to help determine how much methane has been converted into biomass.
The water (principally), ooze and possibly the sidewall-coating fractions are progressively sampled to determine their chemical composition, biomass fraction, their biological types and prevalence, noting that the presence of tiny herbivores, carnivores and pathogens (if present) will affect the results. Changing water turbidity should provide a rough estimate regarding how much biomass was being formed in the water column. Dark operation measurements might be used to remove much of the effects of phytoplankton proliferation as opposed to that of methanotrophs.
Estimates are made of how much methane was converted into biomass at different flake concentrations and possibly compositions over different durations. Optimal conditions are determined.

## Slide 4
Experimental Layout
Mesocosm X
= Experiment
Mesocosm C
= Control
Gas bag
Aqueous
fraction
Ooze
fraction
Methane
Diffuser
Buoyant flakes
Flakes without
the key minerals