## Slide 1: Making Fiztop DZFOs
Sev Clarke July 2018

## Slide 2
PET
plank
PET
ribbon
PET/Ti
diffuser
foil
Sequence of Operations
CONSTRUCTING THE DZFOs
1. Laser cut the mannikin-shaped voids
of the D-Z fluidic oscillators; cut and
remove excess PET to lighten the fiztop
3. Laser slice off the side of the plank to
make apertures at the ‘feet’ for gas exit
4. Laser cut holes in PET ribbon for diffuser voids
5. Fix ribbon to side of plank, matching feet to holes
6. Fix the diffuser foil to cover diffuser voids
8. Cut the now composite plank to lengths to cover the round base of
the fiztop surrounding the AIS and battery, then glue the lengths together to form the circular base, heads/up feet/down, and PET/
titanium diffuser foil covering all in contact with the sea surface.
7. Laser slice off top of plank to make apertures
in the ‘heads’ for pressurized gas entry.
9. Attach a rigid foam disc, containing the micropumps, also a waffled
void disc beneath each for each pump’s output, to the DZFO+ disc
Fiztop
base
Micropumps
DZFO+
disc
Note: some of the laser cuts should be angled to permit easy extraction
of the waste material (but not those cuts on the outside ‘leg’ or ‘crutch’)
2. Seal a thin sheet of PET over the plank
top to keep the pieces in place
AIS
Battery