## Slide 1: Outline for a Fiztop Proof of Concept Experiment
Author: Sev Clarke, 8 June 2019

## Slide 2: Introduction
The Fiztop concept is a conceptual method for helping to restore the ocean and climate to health.
To do this, it is proposed to increase the concentration of nanobubbles in the organic surfactant and particulate-rich ocean surface microlayer (< the top millimetre), thereby: reflecting more sunlight back into space; slightly increasing the cooling shading of the water below; and redirecting sideways some of the solar energy that would otherwise take its heat deep within the water column such that it increases the rate of evaporation, thereby cooling the surface ocean waters still further.
Lightweight, floating and solar-powered Fiztop units would deliver monodisperse (same-sized) nanobubbles generated by fluidic oscillators directly into the microlayer. The bubbles are of such a size (~800nm diameter) that they reflect and refract visible light, but are transparent to outgoing heat radiation, being below its infra-red wavelengths.
The low-cost experiments are to be done safely in a laboratory, with controls to help determine just how effective is the method, and to assess what other effects would likely result from ocean deployment. Approved, controlled and gated sea trials may be done at local, regional and global scales, thereby permitting modifications to ensure optimal net benefit.

## Slide 3: Equipment Requirements
Four, ordinary, cubic, glass-sided aquarium tanks, with glass cover seal
An adjustable light source to simulate different solar insolation intensities
Desai-Zimmermann Fluidic Oscillators (DZFO) to generate nanobubbles
Pumps, power, piping and diffusers
Visible, possibly green, light lasers to determine the presence and approximate zonal concentrations of nanobubbles, particulates and microorganisms
Infra-red camera to detect and record the temperature profiles in the water column, the water surface or microlayer, and the enclosed air above it
Light and humidity sensors and recorders
Natural surface seawater, distilled water and salts to simulate seawater
Flow cytometers and standard lab equipment
A dark blue cloth

## Slide 4
Equipment Setup
Green
lasers
Lengthwise, power
adjustable
light source
Positions for taking
infra-red photographs
with a single camera
for the Control tank
Seawater
Pump
Air pump
DZFO
Flow
cytometer
Warming microlayer
Seawater
tank
Control tank with
distilled water &
salts to simulate
seawater
No microlayer, hence
probably less surface warming
and more deep heating
Infra-red camera
locations for
Seawater tank
Dark blue cloth to
simulate the deep
sea colour
Humidity sensors
Light intensity
recorder
Nanobubbles
More undershine glow may be observed
and measured looking upwards at the
microlayer in the case of the nanobubbled
seawater tank than in that of the water
surface in the Control tank
After a long period of exposure to the
light source, the water in the Control
tank may become fractionally warmer than
that in the nanobubbled tank whilst the
air above should be cooler and less humid.
Removing the glass cover should, over time,
cause the level in the seawater tank to
become lower than in the Control tank
Should the method work, the water
surface in the Control tank will become
of lower temperature than that in the
Seawater tank
Should the method work, the surface
in the Seawater tank will become of
higher temperature than that in the
Control tank, and the air above it
slightly warmer and more humid
Glass cover
Reflected
light
sensors
Note, not shown are two more
tanks located immediately
behind those pictured
Light source may be
moved forwards and
angled to simulate non-
orthogonal sunlight
Fan to simulate
oceanic breeze in
evaporation expt.

## Slide 5: Method
Obtain and set up the equipment
Measure or estimate: the zonal nanobubble-particulate distribution; the reflectance of microlayer and control water surfaces, before and after the introduction of different concentrations of additional nanobubbles; the comparative enclosed air temperature and humidity; differences in undershine; and the zonal water temperature, all under different degrees and durations of illumination. The numbers of introduced nanobubbles might be estimated from the oscillation frequency of the DZFOs, the active pore number in each diffuser, and the duration of their activation.
Determine what effects the introduction of different concentrations of nanobubbles into the microlayer have on solar energy distribution and on microorganism species and concentrations in the Seawater tanks over time. This will require a separate Seawater tank without nanobubble introduction, hence possibly a 2x2 matrix of tanks, with only one of the two Seawater ones being nanobubbled, and two, diagonally-arranged (to aid with insolation equality) distilled water+salt ones.
After completing these tests, and should the experiment have given some prospective results, empty the four tanks, add two lateral dividers in each (making 12 cells), and replace their contents with surface seawater and nanobubbles in three different areal coverage concentrations (2, 4 and 6%), two different bubble sizes (say, 700nm and 900nm), and two different, simulated and averaged, daytime (with nightly breaks) solar radiation levels at sea level (those for the central equatorial Pacific Ocean and the central Indian Ocean at 420S), then remove the glass lids and measure the progressive loss of albedo (reflectiveness) and water level over some months.
Then, possibly attempt to estimate what would be the ocean surface and atmospheric cooling effects of each of these changes if made globally over, say, twenty years.

## Slide 6: Wrap-up
Write up the results as an academic paper and submit it for peer-review and publication.
Coincidentally, submit an early draft to research, government and engineering organizations that might be interested in: its various applications (such as protecting coral reefs); in modelling and optimizing its net beneficial effects; in the approval processes; in risk management (including addressing that of unchecked climate change); in developing the technology; in manufacturing, deploying and maintaining Fiztops or their components; in their logistics or the complementary development of the cleaner-collector drones; or in assessing what other sensors and services might be provided by such a potentially widely disseminated platform.