## Slide 1: DESIGN FOR A MARINE NANOBUBBLE GENERATOR OR “FIZTOP”
FUNCTION: To brighten the sea surface with long-lived nanobubbles, thereby increasing sea surface albedo and cooling the planet
SHORT NAME: FIZTOP, a solar-powered, top-shaped unit that generates long-lasting, ocean brightening fizz just under the ocean surface.
Sev Clarke
March 2018

## Slide 2: INTRODUCTION
In his paper “Bright Water” (2010) https://arxiv.org/pdf/1010.5823.pdf Seitz analysed how microbubbles could be used to enhance marine albedo, thereby cooling the planet.
Nanobubbles last much longer and do a better job.
These can be generated most efficiently using fluidic oscillators.
Buoyant cones powered by photovoltaics and using Desai-Zimmerman Fluidic Oscillators (DZFO) might brighten remote ocean areas safely and cost-effectively with these highly reflective but invisible nanobubbles, whilst shading corals, cooling the ocean surface waters below the sea surface microlayer, and increasing the rate of evaporation and off-planet, longwave radiation by redirecting some of the sunlight sideways into the microlayer.

## Slide 3
DESIGN FOR A MARINE NANOBUBBLE GENERATOR = a Fiztop
0.6m
1.6m diameter
A fizz of ~1,000nm diameter nanobubbles is ejected and diffuse down to 800nm
PET/titanium foil diffusers
Nanotextured, self-cleansing
transparent PET plastic cone
Thin organic soup
Sea surface
Semi-flexible photovoltaics,
made of perovskiten/polymer film
Fluidic oscillators
Concentric rings
of gas micropumps
Battery or capacitor
~350
Surface area of
PVs ~2.5m2
Base-enclosing material may be in
the form of rigid, closed-cell
polymeric foam surrounding the
pumps, tubes and fluidic oscillators
Prevailing wind, when present
Current
Indirect insolation
Reflected insolation
Direct insolation
AIS
One of three floats designed to lift the diffuser outlets to the level of the organic microlayer so the nanobubbles are injected just into it. Alternatively, have the active diffusers inset in the base in strips
Surfactant-rich microlayer
DZFOs
Conical or top-shaped
Fiztop unit
Semi-
inflatable
Copper electroplated
anti-fouling layer
Flexing aerial-sensor
for conditions
Aerial &
Support
Hooded, valved and
filtered air inlets

## Slide 4
FIZTOP UNDERSIDE PROFILING & MICROPUMP ACTIVATION
A
B
C
K
L
M
A
B
C
K
L
M
A
B
C
K
L
M
No wind/Low wind
Moderate wind
Strong wind
Flexing wind sensor
Anchor/sea anchor cable
Microlayer flow
Strong microlayer flow
Micropumps in the C-K ring are activated, plus possibly those B-L ring
or else the downwind L semicircle
Activation status
Surfactants in the microlayer move under the whole fiztop unit
Seawater builds up against the
upwind faces of the fiztop
Micropumps in the A, B, C, L and M semicircles are activated
Micropumps in the A, B, C and possibly M semicircles are activated, the others
might generate nanobubbles too far below the surfactants of the microlayer,
thereby possibly not allowing the nanobubbles to become stabilized in time

## Slide 5: MARINE NANOBUBBLE GENERATORS
Disseminate them mainly in remote subtropical and tropical waters where the insolation is high and the waters are usually calm. Also, over where the waters of the Great Ocean Conveyor Belt/Gulf Stream upwell to the surface, to be carried along it.
Sensors & comms periodically transmit data about Fiztop identity, location, status, and local environmental conditions
If in danger of overturning or overturned by wave or wind, the stabilizing anchor line or sea anchor, weighted base and shape tend to keep it upright or to right the unit if upset
The nanotextured cone surface is made self-cleaning, like some leaves
Upper shape is resilient to normal wave action and provides no perch
Units are collected, cleaned & relocated by drone vessels, as required. As well as their locator systems, the bulk movement of Fiztops could be predicted from wind and current data
Degraded diffusers might be replaced with new ones by slicing through the honeycomb layer just above them and heat-sealing on replacement diffuser foil. The honeycomb PET layer might originally be made thick enough to accommodate several such replacement refurbishments performed by maintenance staff
Nanobubble half-life is likely to be measured in months, when aided by surfactants in the sea surface
Units are light and buoyant enough to pose little hazard to shipping
The under surface will provide algal food and habitat for marine life
Use satellite and aerial surveillance to determine Fiztop effectiveness

## Slide 6: CONSIDERATIONS
There are some practical considerations that will need to be addressed before this concept can be validated, one of which is whether the unit might overheat enough to damage the battery/capacitor or the Artificial Intelligence System (AIS).
Others are: would enough power be generated to produce useful amounts of nanobubbles; would biofilm or marine organisms block too many of the diffuser pores too quickly; following overturn, is the design sufficiently self-righting; what is the unit’s average longevity at sea; will theft or vandalism be a problem; and what is the likelihood of RD&D funding and deployment approval by relevant agencies.
To cope with varying environmental conditions, such as storms, the three optional floats might be inflatable/deflatable at the direction of the AIS.
Note, that such nanobubbles do not constitute foam as they occur beneath the ocean surface, if only by a little. Nor would they tend to agglomerate or coalesce because their exterior surface has the same, repelling static charge.

## Slide 7: Dissemination
Dissemination, cleaning and maintenance of Fiztops in the vicinity of coastlines might best be performed by locals with boat access. These might be fishers or tourism operators who benefitted from Fiztop presence, or else a specialized corps of paid workers.
Anchoring systems, in the form of anchors with attached reels and lines, might be used to fix Fiztops where they would be of best use.
Similar anchoring systems might be used to deploy Fiztops in deeper or remote waters from either larger vessels or cargo planes fitted to allow deployment. Airborne deployment might require the use of water-soluble parachutes. Lines might be made from carbon fibre, graphene or coated Zylon.
Alternatively, large drone or remotely operated vessels (ROV) might be used to perform most Fiztop-related care functions, including that of relocating free-floating ones to better areas and of gathering others for refurbishment or replacement.

## Slide 8: Manufacture of DZFO Diffusers
Commercial diffusers are not particularly well-suited for DZFO use.
They are: too thick, too expensive, too energy-intensive, non-flexing, too heavy, too subject to failure, or typically do not provide pores of the desired shape, numeric density and dimensions for optimal DZFO operation at either micro or nano levels.
Our proposed diffusers suffer none of these deficiencies. Moreover, their manufacture appears suited to large-scale, mass production whereby the basic product, the diffuser plate or porated laminate film/foil, meets the requirements of a full, diffuser product range.
None of the process steps are particularly unfamiliar to current practice, only the scales at which they operate and their combination.

## Slide 9: Draft Process Steps
Grow cubic salt (NaCl) crystals of the desired micron or nano size using the antisolvent crystallization method which generates monodisperse (same-sized) crystals by adding alcohol slowly to a fast-stirred, near-saturated salt and water solution.
Thoroughly dry and mix these crystals into molten PET polymer at the desired concentration to give the diffuser pores the optimal average separation
Calender the mix onto titanium foil ribbon of the desired thickness that is thinly copper-electroplated on one side as an anti-fouling measure. The calender roller next to the foil could be rubber-coated so that each salt cube would indent the foil, thereby making a better funnel to focus the tiny air pulses at the foil end of the pore, minimizing any difference effects in salt cube sizes, and helping to ensure that PET does not obstruct the salt from the dissolving water or the etching acid from the foil.
Ensure the salt surface is exposed then wash the salt from the resulting laminate.
Use additional rollers to add etching acid then later remove titanium etching mixtures of hydrofluoric and nitric acids and their products from the laminate.
So progressively etch the titanium foil that exit pore holes of the desired dimensions are made on the opposite side to the PET.
At some stage electrolytically deposit a copper anti-fouling layer on the exposed metallic side of the PET/titanium foil diffuser sufficient to last until its expected refurbishment date.
Shape the diffuser ribbon and heat-seal or otherwise glue it to a honeycomb of PET to the PET of the DZFO outlets. The honeycomb gives each DZFO leg outlet a fixed area of diffuser to use.

## Slide 10: Diagram of how the pores are made
Cubic salt
crystal
Cubic
void
Lightly
etched
depression
Deeply
etched
depression
Completed
diffuser
pore with
narrow,
~circular
exit
Titanium foil
Laminate of PET (polyethylene terephthalate) polymer and titanium (Ti) foil
Inverted mushroom shape
focusses the pulse of air
towards the exit
In operation, there is here a film of brine or seawater, or the sea surface itself
Ejecting micro/nanobubble may shrink in
water or burst in air to form nanodroplets
DZFO pulsed
air outlet
PET
~700nm
~1,000nm
Process steps

## Slide 11: Finishing
To address the statistically-rare occurrences where salt crystals agglomerate in the liquid PET or where undesirably larger ones have grown, thereby resulting in pores which are undesirably large, the following finishing process is suggested. A thermoplastic, polymeric powder, where the particles have diameters ranging above that of the required pore diameter, is mixed with a miscible, low-viscosity, low boiling point and possibly flammable liquid, such as ethanol. This slurry is then modestly pressurized against the PET side of the perforated, PET-Ti foil such that the pressure is just enough to cause droplets of slurry to pass through pores in the foil that are larger than desired, but not into or through ones of the correct size. As a result, polymer particles would tend to clog the oversized pores. Brush rollers would then remove excess slurry from both sides of the foil. Passing the PET side of the foil through a flame could then be made partly to melt the exposed part of the trapped particles onto the surrounding PET. This process would also tidy up most of the fine filaments of PET caused by crystal crushing and liquid PET intrusion into the cracks during the lamination and salt dissolution processes.