## Slide 1: OCEAN NANOBUBBLES:
Their generation, stabilization and uses
Sev Clarke July 2018

## Slide 2: The Ocean
The ocean is a dilute, organic soup.
Its surface microlayer, of perhaps 20 micron thickness (TBD), is especially enriched in organic, surfactant molecules and particulates.
Such substances are often lighter than seawater and miscible with it, but are so tiny that they are barely buoyant and move upwards only when in aggregations or attached to bubbles, or via turbulence or upwelling.
The organics are continually being destroyed by bacteria or ultraviolet light and are renewed mainly from below by emissions from phytoplankton and higher forms of marine life.

## Slide 3: Ocean Bubbles
Bubbles on and in the ocean tend to be generated by breaking waves, though there are many other ways by which they can form.
Most bubbles, from large ones to those of millimetric dimension, rise to the surface and burst typically within minutes of their formation.
Microbubbles tend to rise to the surface slowly, to last for up to hours, and to disappear rather slowly as the pressurized gas inside them leaks out (osmoses or diffuses) into the surrounding water. Some microbubbles may thus become nanobubbles.
Nanobubbles are different. Given the viscosity of seawater, they are too small to be buoyant unless surrounded by relatively buoyant surfactants or in aggregations called bubstons. Although nanobubbles contain gas at even higher pressures than do microbubbles, leakage is minimal because of three factors: surfactants surround them with protective layers or shells that reduce their surface tension; the gases that do leak out are trapped in the shells so that the water becomes saturated in them, thereby preventing more gas from leaking out; and surrounding the surfactant layers are electrostatic ones composed of distinct concentrations of anions and cations (made from the components of marine salts) and charged particles. Nanobubbles can last for up to periods of the order of a year in the laboratory and probably for several months (TBD) in the sea, the duration being largely a function of the concentration there of surfactants – the higher the surfactant concentration, the longer is nanobubble lifetime, see http://www1.lsbu.ac.uk/water/nanobubble.html .

## Slide 4: Nanobubbles
The sea contains only a tiny volumetric fraction of nanobubbles, perhaps of the order of a millionth or 0.0001% (TBD).
Nanobubbles may be generated by many processes, including: wave action, lightning strike, ship propellers, microorganisms, micrometeorite impact, hard radiation, ultrasonics, microbubble contraction, seabed gaseous emissions, electrochemical reactions, volcanoes, molten rock from seabed spreading, and dark smokers.
Nanobubbles lacking shielding may have a life of only milliseconds.
When shielded nanobubbles are consumed, digestive processes may remove enough of their organic surfactant shielding to cause their oblivion.
In nearly barren (oligotrophic) oceans there are typically not enough surfactants to engender long life for most nanobubbles that are formed there. However, ocean fertilization using buoyant flakes can remedy this.
It is thought that ocean surface nanobubble concentrations may be increased by several orders of magnitude by deploying buoyant, solar-powered fiztops that inject nanobubbles directly into the organically-rich microlayer at the ocean surface.
A modest to high concentration of shielded nanobubbles in the microlayer will not only reflect more sunlight from entering the ocean by increasing its reflectiveness (albedo), but, probably more importantly (TBD), should cause a significant fraction of solar energy entering the microlayer to be reflected sideways within it, thereby typically causing most of that energy to be transformed into heat as it is absorbed there by the soup, thereby causing the temperature of the microlayer, and the few millimetres below it, to increase such that the evaporation rate would substantially increase, thereby over time cooling the waters below by shading and evaporation, increasing the coverage or density of cooling marine clouds, and increasing precipitation downwind.

## Slide 5
Nanobubble
Concentric rings of perpendicular
solar insolation being reflected and
refracted by a nanobubble
% of beam’s cross-
sectional area *
19
17
15
13
11
9
7
5
3
1
Solar energy reflected laterally:
Coded Proportion x Direction x *Area = SubTotal
Magenta 0.94 30% 0.19 0.054
Red 0.70 45% 0.17 0.054
Orange 0.62 92% 0.15 0.086
Yellow 0.66 86% 0.13 0.074
Green 0.58 85% 0.11 0.054
Cyan 0.38 47% 0.09 0.016
Sky Blue 0.12 14% 0.07 0.001
Blue 0.10 10% 0.05 0.001
Purple 0.06 7% 0.03 0
Lilac 0.00 0% 0.01 0
TOTAL 1.00 0.340 or 34%
PERCENTAGE OF TROPICAL SOLAR ENERGY
IMPINGING UPON A NANOBUBBLE AT
NOON THAT IS DEFLECTED LATERALLY
34%
Most of which is transformed into microlayer heat
when the photons are absorbed by organic molecules,
particulates or seawater
Sea surface
Note, the internal reflections
are not shown here. Many
will result in increasing
ocean albedo or greater
lateral deflection.

## Slide 6
370
Solar energy reflected laterally:
Coded Proportion x Direction x Area = Total
L Magenta 0.74 52% 0.19 0.073
L Red 0.40 72% 0.17 0.049
L Orange 0.62 92% 0.15 0.086
L Yellow 0.32 90% 0.13 0.037
L Green 0.27 80% 0.11 0.024
L Cyan 0.27 75% 0.09 0.024
L Sky Blue 0.42 60% 0.07 0.018
L Blue 0.45 46% 0.05 0.010
L Purple 0.75 44% 0.03 0.010
L Lilac 0.78 40% 0.01 0.003
Subtotal 0.334
R Magenta 0.00 0% 0.19 0.000
R Red 0.68 25% 0.17 0.029
R Orange 0.64 34% 0.15 0.033
R Yellow 0.36 60% 0.13 0.028
R Green 0.22 70% 0.11 0.017
R Cyan 0.40 90% 0.09 0.032
R Sky Blue 0.46 88% 0.07 0.028
R Blue 0.20 65% 0.05 0.007
R Purple 0.76 32% 0.03 0.007
R Lilac 0.78 40% 0.01 0.003
Subtotal 0.184
Average 0.259
Note:
Omits correction for
refraction at the ocean
surface
26%
PERCENTAGE OF TEMPERATE OCEAN SOLAR ENERGY IMPINGING
UPON A NANOBUBBLE AT NOON THAT IS DEFLECTED LATERALLY
Nanobubble
Albedo-enhancing
reflections
Sea surface
Insolation rays
Internal reflections
not shown, some of
which would increase
albedo or lateral
deflection

## Slide 7: How to use these deflection calculations
It should be recognized that the tropical zone 34% and temperate zone 26% figures are best-case ones when the sun is at its highest. Average diurnal ones that incorporate dawn to dusk insolation might be approximately only half as effective at deflection, perhaps 17% and 13%. Thus, taking the subtropical zone as the average between the tropical and temperate zones where fiztops are likely to be used, 15% deflection seems a reasonable estimate for where they are to be used.
Now, this figure is a gross simplification as it may not take into account: diffuse insolation; sea and sky conditions, including their turbulence; temperatures; current levels of microlayer warming and humidity; microlayer thickness; varying ‘soup’ composition; winds; currents; whitetops; phytoplanktonic albedo; turbidity; or the different levels within the microlayer where nanobubbles may be located. For the present, it is assumed that the thermal effects of these cancel out.
However, as, ignoring clouds, the average daily insolation at the surface is ~6kWh/m2, even 15% of this, or 0.9kWh/m2, at 3% ocean coverage with nanobubbles would likely provide additional average evaporative surface heating of 27Wh/m2 per day. It should be possible to model the global effects of such, and indeed, to add confirmation by way of laboratory testing.
However, this 27 figure ignores the fact that 700nm diameter nanobubbles are transparent to infrared wavelengths, as they are smaller than them. An estimate from the solar spectrum at sea level graph at https://en.wikipedia.org/wiki/Sunlight indicates that non-IR frequencies contain only ~45% of solar energy. Hence, the 27 figure should be reduced to ~12Wh/m2/day of additional microlayer warming to be caused by the presence of nanobubbles covering 3% of the tropical to temperate ocean surface.

## Slide 8: Considerations of Effectiveness
The effectiveness of nanobubbles to reverse global warming will depend on several factors, including:
  What range of ocean coverage with nanobubbles can fiztops be made to deliver;
  Nanobubble lifetime and its extension by the generation of more phytoplanktonic surfactants in oligotrophic waters;
  How much the presence of nanobubbles can deflect a significant proportion of the heat that would otherwise have gone many metres into the depths, to instead heat the microlayer such that the heat goes into evaporating water which then, in the presence of cloud condensation nuclei (CCN), forms cooling and reflective cloud;
  What is the ratio of microlayer heat that goes into additional evaporation, some of which will thereby go off-planet via longwave radiation, most of which may occur at night and at significant altitude due to diurnal turbulent mixing;
  How well can interventions in the rate of evaporation be used to effect net beneficial, and possibly far downwind, influence on precipitation, soil moisture and weather events such as heat waves, droughts, wildfires and hurricanes;
  The increase in ocean surface albedo produced by the nanobubbles; and
  What level of local, regional and global governance and control over the placement, concentration and operation of fiztops is achievable to deliver desired outcomes.
  The effects of the likely reduction in surface tension of the ocean surface microlayer resulting from increasing its temperature is TBD. One such effect might be that droplets from splashing are more easily formed and could range down to a smaller diameter.

## Slide 9: OCEAN NANOBUBBLE COVERAGE
Modelling is required to establish the effects of covering certain ocean regions with nanobubbles to these levels: 0.3%, 1%, 3%, 10% and 30%.
In the thickness of the microlayer there may be generated many layers of nanobubbles. Thus, ray refractions and reflections from one nanobubble may impact on many others.
The nanobubbles to be generated by the fiztop units are expected to have monodisperse diameters of around 700nm.
Some fiztops are to be moored so that the nanobubbles they generate will be taken by currents to stationary assets to be protected, such as coral reefs. Other fiztops will be free-floating with only sea anchors, for instance those placed so that they are carried along by the warm, surface currents of the Great Ocean Conveyor Belt in order to cool its overheated state, and eventually, the Arctic.
It is surmised that each fiztop will be able to service some 3km2 of ocean (TBD), though with some, but less, effect over a much larger area over time.
Primary effects are surmised to be the enhancement of: evaporative cooling, shading intermediate waters and coral reefs, marine cloud albedo, ocean surface albedo, and targeted terrestrial precipitation control.