## Slide 1: Conceptualising a Low Cost Cryogenic Lab
Sev Clarke, 2 August 2018

## Slide 2: Requirements
SmallTech has been selected to provide theoretical and experimental support for the Ice Shield technology that is being designed to restore the cryosphere and cool our overheating planet.
To do this, a cryogenic lab is required in addition to the SmallTech facilities in Menlo Park, California. The most convenient site for the lab is on the SmallTech parking lot in Menlo Park, or failing that, on the sloping Bay foreshore where there is ready access to seawater, perhaps on a boat ramp.
The aim is to simulate and determine the effects, and to optimize the pumping regime, to create wide, even, and very gently sloping, say at 3-50, ice lenses in sea ice, at the same time as generating ice mass at the fastest rate possible under a range of different, but frigid, environmental conditions.

## Slide 3: Proposed Construction Materials
Either an evenly sloping site of ~80 or a truckload of sand, gravel, or screenings that can be formed into such a slope.
Enough doubled or trebled polystyrene foam sheets to make a closed rectilinear tunnel with total wall thickness of ~12cms and approximate lwh dimensions (5-15)x1x2m.
A ~5,000 litre plastic corrugated tank to hold delivered seawater.
A used freezer unit, possibly from a truck, capable of delivering air at polar winter temperatures, if necessary complemented by a refillable container of liquid nitrogen that could be sprayed into the circulating tunnel air.
Pumps, pipes, valves, nozzles, fans, sensors, recorders, electric supply, cabling, comms, lighting, a narrow ice coring drill or equivalent, a small freezer for the cores, a long extension ladder to act as angled tunnel ‘walkway’ above the ice & water, strapping to hold the tunnel together, glues, sealants and seawater.

## Slide 4
Low-cost Cryogenic Laboratory
Seawater
tank
Freezer
Unit
Liquid
nitrogen
for extra
spray cooling
Grown ice
wedge
Seawater
Brine drain to
measure gas &
salt enrichment
Tapered
door
plug
Circulating
fan
Polystyrene
foam tunnel
Multiple strapping
along the length
of the tunnel
Internal
surface
Road metal, gravel or graded natural slope
Air inlet
Depleted
air outlet
Ice cores taken
to measure salinity
and gas distribution
Pumps
Cold
radiator

## Slide 5
An Alternative Lab Design
Suited to Making Smaller,
Faster and Radial Experiments
Corner of SmallTech Parking Lot
Seawater
Tank
Warm
Tank
Brine
N2
Freezer
Unit
Work platform
Computerised
Control Panel
Current
Experiment
Completed
Experiment
Experiment in
Preparation
Walkway
Walkway
Walkway
Ice
Ice
Thin sea ice on
frigid seawater
Warm
seawater
Seawater
Strapping tensioners stop the walls from bulging
Upper
Level
door
Upper
Level
door
Removable foam polystyrene sections separating the frigid
experiments from the warmer human workspace above them
Sloping ice shield
Frigid seawater becomes saltier
Human workspace
Frigid air in,
warmed air out
Laboratory Cross-section
Slightly sloping foam polystyrene (FPS) roof
Laboratory Plan View
Walls are of 2x~10cm thick foam PS sheeting
Third FPS skin for strength
Geotextile sandwiching bentonite clay lines each triangular tank
~10cm thick wall
Sand, clay, gravel or roadmetal
Chilled
seawater
inlet
Brine
out
Chilled
Tank
Walkways
Walkways
Brine concentration and flow
Pipe
Mixing
Tank

## Slide 6: Advantages of the Design
The cryogenic Lab, materials and equipment can be disassembled and relocated, leaving the SmallTech carpark surface unaffected. This may mean that no Council permission is required.
With three tanks, there need be no wait time between experiments.
Energy left over from chilling is used to warm water, (via an air-to-water heat exchanger immersed in the warm water tank) that is later used to melt the ice rapidly, so that a new experiment can be begun.
Sensor measurements, including the temperatures of the water and ice surfaces are monitored, some by thermal & optical cameras, and their changing morphology by LiDAR. Such real time data might be transmitted to, and displayed in, the adjacent SmallTech offices. These, ice salinity profiles, and fluid flow rates are key inputs for optimizing the intermittent pumping regime.
It is surmised that the data from human operators varying each pumping regime to produce a fast-growing and smooth ice lens under a variety of conditions may be recorded and input to a neural network learning system to generate the AI programs needed for subsequent automation.
Experimenters and visitors in the lab can be at comfortable temperatures, most times.
It is conceivable that other ice research projects, fruitful collaborations or revenue streams might be facilitated by the establishment of the SmallTech Cryogenic Laboratory (STCL).

## Slide 7: Advantages of this Design (cont.)
The volume of water to be processed multiple times can be restricted to little more than that which is frozen.
Most of the controlling can be done either remotely or programmatically, with alerts sent for going off-spec or item failure.
The radial design of the tanks provides a much closer simulation to seawater flowing down the sides of a low-inclination, conical ice shield. Each gush of water should thus spread out into a shallow sheet-like flow that cools rapidly, does not allow an insulating skin of ice to form on its surface, and maximizes gas uptake.
Releasing the icy air flow at the perimeter better simulates the air flowing up the cone (eventually to form a thermal when in open air) and taking the heat of ice fusion rapidly away from the seawater of which the winter Arctic temperature is already close to zero. Of course, the brine temperature may go as low as -200C before it is removed.
The still cold air issuing from the triangular tanks may be passed through heat exchange coils to chill the seawater in the chiller tank to Arctic Ocean temperatures. A mixing tank might be used to obtain seawater at the required temperature for the experiment.

## Slide 8: Design Elements
The geotextile fabric might be as economical as the material used in blue plastic, woven and fused, tarpaulins, provided that the sandwich structure is sufficiently waterproof and ‘glueable’.
Brine, seawater and most of the air flow are to be recycled.
Water salinity can be adjusted by onsite mixing, though some bagged salt may be required.
As the V of a growing ice wedge should be allowed to subside into the seawater, as it would in the open ocean, a fillet should be introduced at the V that becomes smaller towards the base, and the inside walls of each tank should be greased.

## Slide 9: Pumping Regime
What has not been adequately appreciated until now (and that still poorly) is the complexity that will be involved in the development of the required automated, intermittent pumping programs designed to handle changing conditions, requirements, resources, timings, faults, degradations, divergences and perturbations.
It is surmised that for any fleeting set of parameters, there will exist one or more near-optimal responses by the system that are designed to bring the parameters back into a desired line. For instance, if the water flow pulses onto the ice have created an undesirable depression around the outlet nozzle, then a succession of calculated small pulses and separately timed intervals for their freezing are likely to be required before substantial, and possibly directional, gushes can be resumed. Similar is the case should undesirable irregularities occur in the sloping ice surface; or if the ice should begin to build up on one side of the growing ice shield, tilting it more and more; or if the wind should strengthen enough to blow the flowing surface water away from an even distribution; or if available power needs to be rationed amongst different pumping stations; or if more narrow, columnar ice shields are required than extensive ones.
Due to this complexity, and to limited funding until the ice shield concept is proven and widely demonstrated, it is thought that anything more than minor funds should not be committed early on to the hugely complex task of modelling or multi-physicing to ascertain optimal pumping strategies (other multiphysics simulations excepted). Instead, human judgement and ingenuity, tracked, analyzed, and gradually being taken over by an artificial intelligence system (AIS) in certain circumstances, is thought to offer a better initial path.
Until a capable AIS is developed, remote operation of the system by humans is thought to be the best option for the successful deployment of the ice shield technology