## Slide 1: Proposed SERF Experiments
Suggestions by Sev Clarke, 19 Oct 2017

## Slide 2
Forming ice surface
Submersible pump
Form sits on ‘sea-ice’,
sealed at base by
frozen water
Pumping tube with slots for issuing seawater
Braced plywood formwork
Narrow gap at base to allow egress of brine
Low angle of
inclination
GENERIC S.E.R.F. EXPERIMENT
EXPERIMENTS DESIGNED TO:
Optimize pumping regime
Establish feasibility of 3-50 angle of inclination
Ascertain how the ice surface shape can be controlled
Measure how salinity changes within the ice form
Determine how fast can the ice be built up under a given set of weather conditions
Develop fixes to encountered problems such as the pumping tube freezing up
Observe cracking of surrounding ice and sinking of the mini-iceberg – if any.
1-1.5m

## Slide 3
PLAN VIEW OF SERF POOL WITH SEVERAL ICE EXPERIMENTS IN OUTLINE