## Slide 1: How to Grow a Grounded Ice Array
Sev Clarke, October 2017

## Slide 2
W
Wind turbine
Satellite pump
Ice shield/lens with
satellite pump at its
centre
ICE SHIELD ARRAY
A1
A2
A3
B1
B2
B3
B4
B5
B6
B7
B8
B9
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
C11
C12
C13
C14
C15
Grounding pump
LEGEND
Open Ocean
Notes: Ice shields or lenses are grown by pumping seawater onto sea ice using satellite pumping stations arrayed around a central floating wind turbine for renewable power delivery.
Powerlines are supported on tall, thin, wood-composite conical pylons. The base of each is buoyed and temporarily anchored until it can be encased and secured in thick ice. As the ice grows thicker towards the elevated powerline, pylon extensions can be made using socket tangs to any required height/depth. Surmounting each pylon is a removable three-socket tang made of insulating ceramic that holds the powerline. The pylons and powerlines radiate out from each central power source, dividing as necessary.
An ice shield array consists of lenses of grown ice that are hexagonally close packed and fused together around a central wind turbine. For a hexagonal array of 48 lenses, this means that the longest array powerline might be a little more than four concentric circles of ice lenses deep, or approximately 10km long.
Depending mainly on the depth of water and the capacity of the turbine, each turbine may power up to perhaps fifty satellite pumping stations and up to some thirty five grounding pumping stations, typically not all at once. Pumps no longer required for satellite pumping may be redeployed as grounding pumps. These will also tend to become the ice maintenance pumps.
Except for sea ice formation in winter, polynyas between ice lenses that are not required for grounding pumps are left open for wildlife and/or GHG harvesting.
Grounding pumping stations are initiated when the ice array base approaches the seabed. They ensure that sufficient ice is built up above sea level to securely ground the array.
Maintenance winter pumping ensures that ice lost to melting is replaced.
An artificial intelligence system (AIS) ensures that available power is optimally rationed to the pumping stations.
Excess wind turbine power may be used for harvesting, processing and transporting GHGs being emitted from the seabed or is sent by HVDC lines to the nearest grid.
Depending mainly on the depth of ice required, individual ice lenses will tend to be less than 2.5km in diameter and from 40-1,000m in height/depth. However, ice arrays grown to float over very deep water may only be grown and maintained thick enough to withstand expected wave and storm conditions.
Ice arrays may either fuse together, fuse onto land, remain free floating until beached, or form the edges to designated sea lanes and channels for vessels and wildlife.
Some pumping stations will be given the facilities to act as all-weather maintenance, logistics, processing and/or scientific bases.