## Slide 1: Cooling with Salt
How breaking ocean waves help cool the planet and ocean,
and we could enhance this effect using a wind-powered, seawater atomisation, or Seatomiser, system. Furthermore, the same system could be used to sublimate iron salt pellets into a sub-micron iron salt aerosol (ISA) so that it photo-catalyzes the harmful tropospheric pollutants of methane, soot, VOCs, PFAS and ozone, whilst subsequently causing cloud nucleation and precipitation at predetermined locations downwind.
Sev Clarke, March 2021, adapted Sep 2022

## Slide 2: Wave Action, Spray Generation and Location
When waves break they create bubbles, the familiar whitecaps and spume, which burst to form fine droplets of seawater. Turbulence in the Atmospheric Boundary Layer (ABL) tends to loft some of these droplets, or their dessicated residues, high in the troposphere. On reaching supersaturated air, these cloud condensation nuclei (CCN) form or thicken reflecting marine clouds and may produce downwind precipitation.
Sea salt aerosols (SSA) of submicron and low-micron diameter are also generated by the impact of rain and other droplets on water surfaces, see David Cole’s PhD thesis (2007) https://researchonline.jcu.edu.au/2065/3/03Chapter3Part1.pdf. These form via a variety of processes, some of which form droplets of brackish salinity resulting from mixtures of fresh and seawater. On evaporation, these lead to smaller and typically longer-lived SSAs.
Some droplets, or the even smaller salt crystals which they form on evaporation, can be lofted into the atmosphere for days where they reflect sunlight (as either sea fog, salt aerosol or marine cloud), thereby cooling the water below. Furthermore, the evaporation of airborne droplets, the release of their energy of vaporization on subsequent condensation at altitude, and its longwave radiation into space may be used to increase the rate of ocean and global cooling substantially. Most of the condensation and longwave heat radiation would tend to occur at night.
Whilst whitecaps are typically formed by storms, most of the time it is too calm for serious whitecap formation. However, we could use wind power and fog nozzles to spray droplets of selectable size to cool targeted, downwind regions such as coral reefs.
Pumps and spray dispersal nozzles on floating wind turbines could generate wind-blown plumes of reflective droplets and salt particles. These would last until precipitated out. When it was rain that did the precipitating, each raindrop-nucleating salt particle would be so diluted by water condensing on it that the water would typically be less salty than fresh river water. Pumped and sprayed droplets bypass the evaporation-reducing barrier of the thin layer of fully-saturated, humid air that coats the ocean surface, making use of the deep layer of unsaturated air that lies above it. Moreover, the surface area of fine droplets may be several orders of magnitude greater than that of the sea surface below them, thereby hastening evaporation and evaporative cooling still further.
Anchored, upwind Seatomiser units might be used to reduce the radiation that was overheating the waters around coral reefs, thereby preventing them from bleaching. Seagrass meadows, kelp forests, Sargassum, mangroves and mariculture operations might similarly be protected. Ocean stratification would also be reduced. As the reduction of only a few percent of solar radiation is enough to save coral reefs, yet is not large enough to have any significantly adverse effects on other life forms, the method is likely to be a safe one, replicating as it does natural processes.
The additional atmospheric moisture resulting from droplet evaporation would tend to increase precipitation, possibly far downwind. The location, regularity, evenness and extent of such precipitation might beneficially be influenced by the concentration and selectable size of seawater droplets produced by Seatomisers.
Given the increasing tensile strength of new polymeric and nanocarbon materials, and the ways of smoothing transient strains imposed on anchoring cables, it is surmised that anchoring could be effective in waters up to some kilometres deep, and possibly in most waters.
Free-floating Seatomiser units could be useful in deep ocean waters where circular gyres or currents, such as the Antarctic Circumpolar Current, tended to keep them from beaching or interfering with shipping lanes. Such units would need to be used where iceberg impact or moving sea ice could affect anchoring. Any units that broke out of such confining currents might be identified from their beacons and towed back into the fold.

## Slide 3: Contributions to Sea Salt Aerosol Formation
No paper has yet been located that authoritatively allocates the contributions of the various natural means of generating SSAs. These means include those: from bursting bubbles of the film, jet and spume kinds; from liquid droplets to liquid surface impacts; from secondary effects of both of these mechanisms, such as the generation of small-sibling or daughter bubbles and droplets and their subsequent effects; and from other mechanisms.
Droplets of the desired size(s) might best be generated by means such as BETE.com’s bi-phasic, SpiralAir nozzles using increased liquid and gas pressures to reduce droplet diameter, or possibly including by making them tri-phasic so that effervescence can help reduce droplet size. Whilst BETE offers several options for the material forming the nozzles, because of the high corrosivity of seawater, the very high pressures likely to be used, and possibly to minimise decavitational abrasion, it may be useful to use their most durable nozzle material options, such as titanium or tungsten carbide, and to coat the internals of each nozzle with a diamond or a diamond-like coating (DLC). For this to occur on the inside of a nozzle, the spiral may need to be coated separately and the mixing chamber may needs be formed from two halves, divided lengthwise, coated, then joined.

## Slide 4: How Might Cooling Be Achieved with Sea Salt?
The key to doing this may be in generating fine sprays to generate enhanced evaporation, useful shading and albedo effects, and controlled precipitation - and to do this in a safe and cost-effective manner. Amongst other methods, modified fogging nozzles may be best suited for the purpose.
Floating wind-powered turbines, pumps & nozzles would deliver large plumes of fine seawater droplets at different heights above sea level. The ones released highest would be crafted principally for albedo-enhancing purposes, the lower ones for evaporative cooling. Stored energy could even out power delivery when the wind was insufficient.
There are five main cooling effects obtainable by seawater spraying: enhanced evaporative cooling with condensation at altitude; sea fog generation by way of the droplets, saturated air and condensation nuclei; solar reflection by sea salt aerosols; marine cloud brightening (MCB); and the reduction of insulating, winter Artic cloud by the introduction of Aitken-mode aerosols. Such cooling would be partly offset by increments in the atmospheric concentration of the greenhouse gas, water vapour, and in the downwards longwave reflection from any additional cloud, fog and the sub-micron particulates.
At an average global ocean wind speed at 100m height above sea level of ~9.0m/s, or 32km/h, a modestly-sized wind turbine of, say, 2.5MW rated power, with a rotor diameter of 100m, and mounted on a hollow, toroidal, steel or reinforced concrete buoy, with supporting spar, struts and anchoring cable should be sufficient to generate plumes of low-micron droplets and sub-micron SSAs to form a reflective aerosol covering 32x24x6x0.1 = 460km2 that spreads out to, perhaps, as much as 3,000km2 via wind, diurnal turbulence of the Atmospheric Boundary Layer, and diffusion over its average 6 day life, but thinning out as it gets further from the point of dissemination. Its effect on increasing albedo would likely be considerably greater should the expanding aerosol plume encounter saturated air where it would form or brighten marine clouds.
Now, a 2.5MW Seatomiser unit with an average power output of 1MW should be able to pump seawater up to 100m height and to use 100atm of pressure to spray out droplets at an average rate of up to 90 litres/sec (say 30 litres/sec to allow for losses and the use of higher pressures to obtain smaller droplets). Over a year it would have pumped 30x3600x24x365 = 946m litres or ~950,000m3 of seawater, of which some 0.6Mm3 might become atmospheric water vapour, 0.3Mm3 brine fog that fell back into the sea within a few hours, and 0.05Mm3 that became aerosolized as long-lived (days) reflective sea salt aerosols (SSA), cloud condensation nuclei (CCN) droplets, or iron salt aerosols (ISA).
As ship track aerosols or ‘contrails’ have been shown photographically to disperse over an average area of the order of magnitude of 3,000km2, it is surmised that Seatomiser SSA and sub-micron droplet plumes might do likewise. However, during this time, precipitation losses might amount to perhaps 30% of the volume pumped, to produce a gossamer thin, reflective aerosol layer. Reflecting probably less than an additional, average 2% of incident sunlight in the area covered, such a small percentage change would be unlikely to have significantly net adverse effects on photosynthetic, other organisms, or even on photovoltaics or sky colour.

## Slide 5: Cooling (continued)
For the solar forcing effects of sea salt aerosols, see the paper by Srivastava and Satheesh (2016), which estimates for the Arabian Sea that, at the sea-surface, short wave cooling by sea-salt aerosols is 40 W/m2, whereas long wave heating is only 9W/m2, giving a net cooling effect of 31W/m2. Because of the complex nature of estimation for different seasons, locations, elevations and particle sizes, none is made here of the prospective extent of the global net cooling effects of Seatomiser-generated seawater and sea salt aerosols. Modelling should provide some better answers. However, it may reasonably be surmised that the potential magnitude of the net beneficial effects is large.
As the marine cloud brightening (MCB) effect of any Seatomiser aerosols that managed to reach cloud-making altitude and supersaturated air is similarly complex, the net cooling effect of these is similarly not estimated here. However, because considerable additional cloud-making water vapor would be introduced into the lower atmosphere by distributed Seatomiser units, the albedo effects could also well be substantial.
The most substantial cooling effect per year per Seatomiser unit might, after losses, be half of the heat of vaporization of the 600,000m3 of water each disseminated, or 600,000x106x2,256/2kJ = ~0.68TJ. Over the 25 year average lifetime of a wind turbine, this would amount to some 17TJ by which the surface ocean water and atmosphere might be cooled by the evaporative cooling and subsequent heat radiation into space of a single Seatomiser installation. The other cooling effects might increase this to 34TJ.
It is understood that cooling surface waters by only a few degrees should be sufficient, not only to avoid coral bleaching and heat stress, but also to reduce the number and intensity of extreme weather events, such as hurricanes, floods and storm surges. When felt on land, the additional cooling and smoothed precipitation should also reduce heat stress, flooding, wildfire, disease and drought, and be likely to improve freshwater resources, cropping and forest growth.

## Slide 6: A Seawater Atomiser, or “Seatomiser”
Key requirements for a buoy-mounted, wind-powered Seatomiser are:
That over its expected lifetime the system generates sufficient cooling to justify its development, production and deployment; that its deployment provides net positive benefits to humanity and the biosphere; and that its structure and materials are designed with environmental performance, safety, sustainability and economy in mind.
That a Seatomiser’s current position and status, together with any local environmental information that its sensors collect, can be uploaded regularly, thereby minimizing risk and adding co-benefits.
From the Wang et al. (2017) paper, https://www.pnas.org/content/114/27/6978 , it appears that seawater droplets in the range 5-20µm diameter might best be produced using fogging nozzles. Tri-phasic fogging nozzles running at much higher pressures than is usual might generate <2µm diameter droplets, and thence possibly smaller droplets by partial evaporation and sub-micron SSAs by full dessication. Experimentation and modelling should confirm the effectiveness and effects of such droplet production.
Should the spray be formed from a row of nozzles, each producing a horizontal, fan-shaped spray, then limited gravitational settling thereafter should enable partial separation of the cohorts of different-diameter particles, the smaller ones typically thereafter being lofted highest by turbulence and lasting longest.
Whilst useful sunlight reflection and shading by SSAs might last for several days in dry air, condensation nuclei useful for marine cloud brightening would typically last until they were rained out. MCB is said to be most effective using cloud condensation nuclei (CCN) in the diameter range from 0.06-0.5µm. However, droplets generated for temporary fog production and evaporative cooling would probably use slightly larger modal droplets, much higher liquid flow rates, and conical sprays disseminated well below the MCB ones, so that they did not interfere with MCB.
Iron salt aerosols (ISA) comprised of a possibly lightly gelated or thixotropic slurry of ferric oxide powder (Fe2O3) and ferric chloride (FeCl3) aqueous solution could be sprayed into the atmosphere to clean it of pollutants, such as methane, NOx, soot, VOCs, PFAS and ozone. This concept is a variant of that proposed by Franz Dietrich Oeste et al. These aerosol particles could probably be generated from modified BETE nozzles in particle diameters of 1-5µm, that might then evaporate down to 0.7-3µm in diameter, a size sufficient to keep most of them airborne for days.
Preliminary and unchecked calculations indicate that generating a few megatonnes/yr of nebulized ISA would be sufficient to offset current global methane emissions. The iron required would be ~0.1% of steel production in 2019.
As an alternative material option for atmospheric methane and smog destruction, possibly more suitable for terrestrial application, aqueous nanoparticles of titanium dioxide (TiO2), might be useful in photo-catalyzing airborne methane and smog there. The feasibility and effects of disseminating this material by similar means should be investigated. Rained out on solid surfaces, it might continue its beneficial photocatalytic effect, plus adding to UV albedo – but it might have deleterious effects.

## Slide 7: Options for Airborne Methane Destruction
There are at least three options for oxidizing airborne methane:
The cheapest may be to separate particles of, say, <3µm diameter from red mud waste (comprising ~42% Fe2O3 & 4%TiO2) by hydrocloning, then to spray it into the air with aqueous ferric chloride (FeCl3) in low-micron droplets. Note, that TiO2 particles can also act photocatalytically on methane (CH4). The hydrocloning might best take place as the slurry emerges from the alumina plant. That way, costs could be minimized and the larger red mud particles (3-30µm) could be partly dewatered and diverted to become input to the Buoyant Flake process. It is TBD whether adding ferric chloride to the slurry containing the smaller particles would help them to be dewatered by flocculation and coagulation. If not, then dewatering to a paste might best take place using the two-fabric, conveyor belt pressing method.
Alternatively, >95% pure Fe2O3 particles with particle sizes <44µm diameter might be sourced from cement colouring suppliers and used in experiments (possibly after further sieving or cycloning). However, this material might well be too expensive and too coarse for large-scale deployment. Instead, raw 93% pure Fe2O3 hematite fines of <6.3mm diameter available from Port Hedland might be first hammer-milled, then bead milled in seawater down to low-micron or sub-micron size, using excess renewable energy, to bring the bulk, FOB cost down to as low as, perhaps, USD$300/tonne. Note, that Oeste et al. show how methane oxidation can occur rapidly using such ferric oxide nanoparticles as the substrate for aqueous ferric chloride, the combination of which in in sunlight regenerates photocatalyzing chlorine atoms.
Finally, airborne ferric chloride particles in the range 20-50nm diameter might be sublimated at ~3150C in heated crucibles atop Seatomiser units from pellets of the anhydrous salt delivered there pneumatically. Anhydrous price is ~$600/tonne. This method has been proven to work by physicist, Peter Fiekowsky and others.

## Slide 8
DESIGN FOR A SEATOMISER USING
SEAWATER ATOMISING SPRAYS
Fender
Seawater
pump and filter
Solar radiation
Reflected energy
<2.5µm seawater droplets may evaporate down to
smaller and saltier ones, or else to <0.6µm SSAs
Six pipe-struts support
the hollow ring
Droplets
Salt crystals
Disseminator
assembly
Flat fan nozzles on horizontal
delivery bar for fine droplet generation
* Artificial Intelligence System
Wind turbine
Struts
Battery
Hollow toroidal buoy
Anchor cables
Weights
Spar
Blade
Air pump
High pressure seawater
pump and filter
AIS*
Comms
Full cone nozzles for extra evaporative
cooling in high winds with
droplets <10µm
Hollow cone producing nozzles for sea fog (1-20µm) + haze
(0.01-1µm) generation & evaporative cooling in moderate
winds. Might generate droplets of diameter <7µm
Wires strengthen the
‘bike wheel’ structure
Fluid delivery pipes
or hollow struts
Tube fits over the nacelle end
to secure the disseminator to it
Nacelle
Side view
Sea anchors &
graphene strap
lightning rods
Using either flat fan spray nozzles
or sublimation to make ISA aerosols
In polar seas this might
require auto de-icing
capabilities
Toroidal tank for slurry
of Fe2O3-rich powder and
FeCl3 aqueous solution
Tower
Tank for gasified
seawater
As the lightning rods may
not survive lightning strike,
they might be replaced
economically using
powerful, quadcopter
drones
Anti-bird spikes might be
useful on the wheel & struts
Flow from captured
Coarse droplets
The ring tube cross-section
might be streamlined to
reduce stress on the tower
It may be more energy efficient
to have the major seawater
pump as direct drive from the
turbine, rather than via the
generation of electricity

## Slide 9
Device to gasify
seawater prior to
nozzle dispersal
Sprayed water
absorbs gas
Pressure kept at, say, 40-50atm
Filtered
air
inlet
Controlled release
air outlet replenishes
the more-soluble
oxygen content
Gasified seawater (or stored spray
solution) at moderate pressure
Spherical or toroidal,
pressurized container
Pump
~0.1mm
seawater
filters
Pump
Manifolds for
gasified seawater
and air
SpiralAir nozzles
Should be able to
produce drying
aerosols of
selected mean diameter
from 0.05-2.0 microns
Filtered
Air inlet
Pump
Spray
Pump
AIS
Gasified seawater
at, say, 40-150atm
pressure
Air at, say,
50-150atm
Note, the gasification should
result in finer particles being
produced from the nozzles,
that therefore stay in the
atmosphere for much longer,
and some of which may be
lofted high enough to generate
or thicken marine cloud
The Artificial Intelligence System (AIS)
is able to optimize the number of
activated pumps and sprays, as well
as the fineness of droplets to suit the
conditions and requirements. Sensors
will also identify malfunctioning elements.

## Slide 10: Prospective nozzle configurations
Many firms produce spray nozzles for fogging, evaporative cooling and similar purposes. So far, the most prospective ones identified are those from BETE.com in their SpiralAir® range (also Schlick), in particular those capable of high-flow and air-atomization. These use a three-stage atomizing process with the energy of the compressed air being the principal atomizing agent.
Whilst a BETE product can deliver 80 L/min of liquid using 7.0bar air and 8.0bar liquid pressures (that might deliver droplets of mean diameter ~15µm), it is surmised that using air (and liquid) at considerably higher pressures (perhaps twentyfold higher ones) might be able to generate seawater droplets as small as 1-2µm in diameter that would then evaporate down to droplets and sea salt aerosols (SSA) of the near-optimal size to be lofted by turbulence to where they would generate or brighten marine cloud at altitude. An alternative nozzle product is manufactured by Schlick, see https://www.myschlick.com/en.
Should even smaller droplets be required, then a nozzle modification that allowed air under high pressure to be dissolved in the liquid, prior to its release inside the nozzle, as effervescence might accomplish this. Care would be required here, so as to avoid successful cavitational and decavitational attack on the nozzle materials. Adding a diamond coating to the internals of the nozzle may well be advisable.
Different nozzles and spray patterns would be required for the different purposes mentioned: a horizontal, fan shaped pattern for the finest seawater droplets and aqueous ISA generation; a hollow, conical pattern for fog generation; and full cone spray pattern for maximum seawater evaporation and subsequent offshore, residual brine precipitation (to avoid land salinization).
As BETE offers several options for its nozzles, or their components, that use materials of higher durability than plastic, brass, nickel alloy or 316 stainless steel, materials such as cobalt alloy 6, titanium, tungsten carbide or ceramic, one or more of these, plus diamond coating of the internals, are likely to be required. Both titanium and tungsten carbide form a strong bond with diamond.
SSAs of large size would tend to dry-precipitate out before they formed rain. Smaller droplets, partially dried (including freeze-dried) and fully dessicated SSAs, and ice crystals would tend to remain airborne for minutes, hours, a day, or a week or two, depending on their size and atmospheric conditions.
All sprayed droplets would initially form a mist before wet and dry deposition and evaporation thinned it out, leaving behind thin, but typically highly reflective aerosols.
Filtered seawater might be sourced from the sea surface or a very shallow depth, where the presence of surfactant aliphatics and other semi-buoyant organics contributed to lowering the surface tension of the droplets, thereby making smaller ones easier to produce for a given nozzle configuration, seawater conditions and pressurization.
Should small, Aitken mode aerosols be achievable by these means, then Salter asserts that we could reduce the winter cloud fraction in the Arctic (and Antarctic), thereby increasing radiation off-planet (substantially). Such would be a most useful contribution.

## Slide 11: Whether and How to Develop a Suitable Baffle System
The first question to answer is whether a baffled system would be useful or necessary. As the commercial nozzles available might not generate a flat enough plume to allow effective gravitational separation, and as using much higher gas and water pressures to generate small enough seawater droplets from the nozzles for our several purposes may cause the resulting plumes to diverge undesirably vertically or to contain too large a percentage of Coarse droplets. A baffle system might be devised to address these potential problems. On reflection, designing such a system may well be a complex task and one in which the design may need to change for different nozzles, pressures, droplet sizes and effervescence. Later sophistications might involve complex fluid dynamics, design by computer, varying structural shapes, representative particle path tracing, and modelling.
It is suggested that simplifying modelling assumptions be made for the early designs. These might include: to limit the droplet sizes to only two, a Coarse one to be captured by the baffle system (of, say, 5 micron diameter) and an Accumulation mode (say 0.5 micron) one to be released to do the cooling work; assume the internal pressure in the nozzle is, say, 100bar, (the nozzle manufacturers using only several bars, whilst Armand Neukerman’s nozzle uses 250bar); and possibly assume that no heating, cooling, aggregation or evaporation occurs in the plume.
For the first few prototypes, it might be simplest just to design the shapes of the baffles and supports by eye or hand to estimate the acute angles at which the parts of plume should impact each baffle in order to effect: the capture of the Coarse droplets only; little interruption to the flow of the plume; to improve its shape; and to direct captured seawater away from the plume.

## Slide 12: How Might One Construct the Intricate Baffle Shapes
Intricately curved shapes are difficult to manufacture. It is thought that using a graphics package, followed by 3D printing, might be a good way to begin for either each baffle individually, or else for the whole baffle assembly. Should the printing be done using a relatively soft material, such as a polymer, and should the operating surface not be of the requisite smoothness, then it might be abraded smooth, then possibly given a hard coating, such as would be given by electroplating a chromium finish onto it. Should such a finish have insufficient durability for long term use, then the substrate might be replaced with titanium or tungsten carbide (both options for the BETE nozzles) followed by giving the working surface of the baffles a diamond coating.
Modifications might then be made to the design to correct any perceived design suboptimalities. Subsequent experiment, modelling and analysis might then be used both to bring the design closer to optimality and to adjust it for different operating conditions, materials and outcomes.

## Slide 13: Spray Conditioning
Although the thin film of spray plume will be exiting the nozzle at a high velocity, its residual pressure would still tend to thicken it undesirably. In addition, the plume will contain an undesirable proportion of Coarse droplets. Both problems might be addressed at the same time by a customized baffle assembly attached to the nozzle supports. The baffles are so shaped and located as to constrain the thickening at what is possibly several centimetres from the ~600 flat fan nozzle. Each baffle is set at a very low angle to the direction of spray and is curved enough that either the upper or lower half of the spray plume emittance direction is intercepted such that the momentum of coarse droplets is sufficient to take them out of the plume and become part of the water slick covering the baffle, then to be conducted further away from the plume by the downwind shape of the baffle. Smaller droplets do not have sufficient momentum to exit the plume and are hence carried along with it. The plume is then intercepted by the second baffle which similarly removes the coarse droplets from the other half of the plume. The removals are effected by the part-cyclonic movement of the plume caused by the curved and angled baffles which causes heavier droplets to impact on the baffle surface and probably be captured there. Such impacts just might have an additional positive effect if they were to result in finer droplets being splattered off the baffle surface, or alternatively, if they resulted in even larger droplets than those impacting being ejected from the baffle surface which were thus more easily removed from the plume by subsequent gravitational settling.
When the post-baffle plume has lost its initial, nozzle velocity as a result of air resistance, it should have little tendency to thicken further and therefore be in suitable form for the commencement of a modicum of gravitational size separation of its droplet population. Such separation will be hindered by daytime atmospheric and blade-induced turbulence, but should be less hindered at night when atmospheric turbulence and lofting of the plume to overhead cloud cover is reduced.
The large droplets resulting from the water slick on each baffle reaching the edge of the baffle, and possibly travelling along it to its tip, should preferably be collected and piped back to the sea or else (less preferably) be allowed to fall back into the ocean, well-separated from the plume. Whilst this water represents a loss of pumped seawater, the additional cooling made by having a thin, horizontal film of non-coarse droplets and subsequent marine cloud brightening should more than make up for the loss.
As passage through the baffles will probably result in a plume direction that is not normal to the plume being ejected by the nozzles, the nozzles themselves could be tilted so that the final plume direction is horizontal (unless a direction slightly upwards is preferred).

## Slide 14: Spray Conditioning (continued)
As the spray conditioning system will preferably need to cope with a range of bi-phasic pressures, plume expansions, and exiting plume velocities, it is thought that the baffle system might be improved by making its operation better able to cope with such variations. This might possibly be achieved by having the baffle assembly spring-loaded such that, as the momentum of the exiting plume increased, it would push the baffles further away from the nozzle. With a thickened entry way to the baffles, this should allow the velocity at which the plume encountered the baffles to be more standardized and hence the cyclone effect also to be more standardized, thereby removing roughly the same-sized Coarse droplets from the plume, whilst the greater bi-phasic pressures generated a smaller, modal droplet size. The ability to use changing bi-phasic pressures would be critical to exerting influence over the location of downwind precipitation, as well as to adjusting the plume and its reflective and evaporative qualities to changing atmospheric conditions.

## Slide 15
Expanded Baffle Design and its Expected Effects
600 Flat Fan
spray plume
Upper curved baffle
Lower curved baffle
Nozzle and
supports
Strut bonded to nozzle supports and both baffles
Droplet plume, now with most coarse droplets
removed, thinned and made more planar
Remaining Coarse mode droplets will begin to sink
out of the plume, leaving behind Accumulation and
Aitken mode ones that may grow by absorbing more
water vapor from the now-saturated plume.
Red and green representative droplet tracks
showing how the baffles modify their paths
Seawater film from Coarse droplet impact on the baffles is captured in grooves
and then is sucked into pipes that direct it back to the ocean, away from the spray plume
The plume widens out and becomes more
convoluted as it moves downwind in turbulent air.
.
Plumes from adjacent nozzles
will eventually overlap
Some droplets and SSAs will be lofted to cloud-making altitude
Baffle assembly may be spring-loaded
so that different bi-pressures and
momentums of spray plume
emission might be captured and
conditioned by the assembly
The cycloning effect of the baffles
removes Coarse droplets from the
spray plume and thins it so that any
remaining Coarse droplets sink
rapidly out of the plume

## Slide 16: Uses of the different spray materials
Filtered seawater is used to generate evaporative cooling, solar-reflecting fog or long-lived sea salt aerosols, to generate or brighten marine clouds in the troposphere, or to thin heat-reflecting clouds in polar winters.
Powdered ferric oxide mixed with possibly a lightly gelated or thixotropic aqueous ferric chloride solution is sprayed to form Iron Salt Aerosols (ISA) that, in sunlight, form the photocatalytic chlorine atoms and hydroxyl radicals that destroy atmospheric methane, smog, volatile organic compounds (VOCs), polyfluorinated alkyl substances (PFAS), NOx, ozone and black carbon. The subsequently-deposited iron content would also feed phytoplankton.
Alternatively or as well, nano particles of ultrafine titanium dioxide (possibly lightly and thixotropically gelated to keep them from settling or agglomerating in aqueous media) also act as catalysts to clean the air of many pollutants. Landing on solid surfaces, they may continue to operate thus for long periods. Nanoscale TiO2 is transparent to visible light but absorbs UV light. In the presence of UVA (black light) in the 365-385mm wavelength range, or UVC light in the 185-254mm wavelength range, the nanoTiO2 catalyst particles are excited and react with water molecules to produce short-lived, hydroxyl radicals that destroy many pollutants, particularly when the humidity is >60%. The 185mm UVC does generate ozone, but this requires cooler, less humid conditions.
Tungsten and copper compounds are needed by methanotrophs in the sea, lakes and soil that consume methane, turning it into biomass. These compounds might best be disseminated by Seatomiser or Ice Shield wind turbines located in polar and some sub-polar regions, and by land-based Seatomisers.
Some polyvalent anions (such as silicate and phosphate) can help raindrops to absorb, and thence deposit, CO2 in the surface waters faster than otherwise (by scrubbing the air), where it and the anions can be used by phytoplankton to make biomass. These could be added to the pressurized seawater from separate tanks. Otherwise, the IPCC reports that the atmospheric lifetime of CO2 in the atmosphere ranges from 5-200 years, depending on the removal process.

## Slide 17: Some subsequent concept improvements
It was realized that, in many cases, the spraying unit is better if mounted on a separate, floating unit. This arrangement would also allow Seatomiser units to be interspersed amongst existing wind farms or in new, composite arrays. Several such spray & sublimation units might derive their power from a single floating wind turbine.
As in the diagram on the next slide, the visible portion of each spraying unit might resemble the mast and spars of an 18th century wooden warship, whilst being constructed of different materials for different purposes. The semi-submerged and submerged portions might resemble the supporting toroidal buoy and spar of the floating wind turbine design.
The sprays and sprayed areas would be altered according to the wind direction, the weather forecast, and the desired downwind effects in each.
On occasion, the CCNs generated by ferric chloride sublimation might replace those of the flat fan spray nozzles and winnowing, or vice versa.
A key feature of this revised concept is that the plume of humidified air is kept largely separate from that of the warm CCN plume until the humid air has become supersaturated at higher, cooler regions, and thus becomes amenable to marine cloud formation as it finally mixes with the CCNs. This also would tend to prevent the CCNs from being prematurely captured by falling brine droplets.

## Slide 18
er
Seatomiser (seawater atomisation) System
Floating wind turbine
on buoyed and
weighted spar
Floating mast structure
With 4 spars, 3 to spray
seawater droplets and
one to sublimate iron
salt aerosols (ISA) to oxidise
atmospheric methane
and nucleate cloud then
rain or snow far downwind
Power cable
Pumps
Fan-forced, heated crucibles generate
20-50nm ISA from pneumatically-delivered
FeCl3 pellets @ ~200m altitude. Later on
these ISA will nucleate more cloud & rain
Sprayed and winnowed ~2 µm modal diameter droplets become cloud-condensing nuclei (CCN) & reflective, 500nm sea salt aerosols (SSA).
~10 µm droplets partly
evaporate to humidify
the air and fall as brine
back into the sea.
~12 µm droplets are
used in strong winds
for the same purpose.
Cooled and oxygenated brine
droplets fall back into
the sea before reaching land
Saturated air and CCNs are taken by
turbulence upwards to cloud-forming altitude
Winnowing baffles
Chlorine atoms destroy
atmospheric methane
photocatalytically
Condensing water vapour
releases heat into space,
cooling the planet
Seagrass Meadow
Mangroves
Coral reefs
Shellfish beds
Surface waters are
cooled by shading
Generated sea fog
and saturated air
Ferric chloride
pellet storage
Additional, gentle precipitation recharges aquifers, snowpack, rivers and water stores
Parched land receives additional mist &
rainfall that regreens it whilst mitigating
wildfire, heat stress and drought
Increasing the pumping pressures to the triphasic spray
nozzles reduces the droplet size, thereby increasing
the droplets atmospheric residence time
Unsaturated air
moving landwards
Microdroplets increase the water surface and
evaporation rate by orders of magnitude
External
maintenance
pod
35-100km
Kelp
Air is cooled by
substantial
evaporation
Weather
vane

## Slide 19: Seatomisers to remove greenhouse gases
Adding tungsten and copper salts to the sprayed mix would tend to favor methanotrophs (methane eaters) growing in the water column, rice paddy mud, seabed ooze, melting permafrost or soil.
The ferric chloride aerosol spray might occur best during morning hours to minimize wastage, to take advantage of diurnal turbulence in the Atmospheric Boundary Layer, and of the catalytic effect of sunlight.
To enhance Seatomiser economics and reach, it might also be possible to retrofit Seatomiser equipment onto turbines in existing onshore and offshore wind farms, both fixed and floating types, or onto offshore drilling platforms.

## Slide 20: Seatomisers to water the land
As well as cooling ocean surface waters, coral reefs, seagrass meadows, kelp forests, mangroves and mariculture operations, together with reducing the severity of storms, hurricanes and sea level rise, Seatomisers might also be used for the primary purpose of improving or smoothing terrestrial precipitation.
For this purpose, they would need to be located such that winds would carry the additional atmospheric moisture and cloud condensing sea salt aerosols over target lands. This condition might not be an arduous one, as both Drs. Stephen Salter and Ben Parkes have shown how precipitation can be influenced by aerosol introduction up to halfway around the globe.
The size, nature, altitude, volume and size distribution of the added aerosols, their concentration, forecast atmospheric and ocean conditions, and topography would all play a part in determining the timing, location, duration and intensity of the resulting precipitation.
Seatomisers used principally to water the land would have further benefits, the main one being that the brine droplets falling through the air into the sea would also be oxygenated beyond that of the seawater they came from. The heaviest brine falls might occur at roughly the same distance downwind of the line of Seatomisers. Even when mixed with some pre-existing surface water, its increased density from evaporative cooling and increased salinity would make it sink, thereby oxygenating the water column to the depth the cool, mixed brine flow made the water sufficiently denser than its environs. In addition, it might even make a useful contribution to increasing the flow of overturning currents.

## Slide 21: Precautions
ANTI-FOULING. Where the sea and machinery are concerned, fouling is usually a key concern. Seatomisers are no exception. The filters, pipes and nozzles will need to be protected from marine growth, corrosion and obstruction. A combination of three measures is proposed. Filters and pipes in contact with seawater can be made of corrosion resistant material, such as titanium or carbon fibre. Every three days or so, these could be flushed with seawater, heated to near boiling temperature, to kill algae and encrusting marine organisms. Subsequently, the equipment might be infused then flushed with strongly-acidic, ferric chloride solution from a separate reservoir to dissolve carbonate-based materials and to kill such organisms as barnacles, starfish and shelled organisms. High-pressure back-flushing and scraping might be used to clear plastic pollution and solid material from the filters.
SYSTEM SENSORS. These would inform the AIS of other threats, problems or conditions requiring attention from maintenance staff or others. A diverse array of sensors, drones and comms, based on the Seatomisers, might provide valuable additional services to the maritime and marine science communities.
BEACONS, LIGHTS & ALERTS. Seatomisers should be equipped with equipment useful in vessels avoiding contact. In addition, turbine blades might be equipped with coloration, lights and sonics to warn off birds.
LEAKING BUOY. Should the toroidal buoy spring a leak or be breached by collision, in order to avert the Seatomiser sinking, it may be useful to provide an inflatable alternative buoy to provide temporary support until the damage can be rectified.
ROGUE OR KILLER WAVES. These are now known to result from certain rare conjunctions of intersecting sea states and winds. The main protection from such waves will be the height above water of the lowest (possibly tilted) portion of the dissemination assembly. Although rogue waves at sea are not known to exceed 32m in height from crest to trough, because sea state extremes are expected to increase with global warming, it might be wise to make the distance somewhat larger than the usual dimension of lowest blade tip (or dissemination assembly) being ~35m above the sea surface for a 2.5MW wind turbine.
ICEBERGS. These might be more likely to push a Seatomiser away, to break its anchoring lines, to breach its supporting buoy or to interfere with its stability. The little defence feasible might consist of the AIS severing the anchor lines before impact, thereby possibly avoiding Seatomiser destruction.